## Slide 1: INFN activity – Reminder of the R&D program
GOAL:
further improvements of the hybrid MPGD (= 2 (TH)GEMs +
1 MICROMEGAS, 3 stages in total) MPGD for single photon detection for
  PID, in particular high momentum RICHes
  Synergies with TPC sensors by MPGD technologies
The starting status (COMPASS RICH upgrade):
Scheme of the detector architecture
The resistive anode by discrete elements
TASK: “Further development of hybrid MPGDs for
single photon detection synergistic to TPC read-out sensors”

## Slide 2: INFN activity – last 6 months
3 tasks on-going :
the development of the resistive MICROMEGAS prototype with miniaturized pad-size
    Design & construction completed
    Pad size: 3 x 3 mm2, pitch 3.5 mm
    Modularity for extendibility: for each group of 128 pads, read-out and services make use of an area as large as the pad group itself
  Read-out via SRS by the original DAQ system Raven
    LabView based, developed for larger band width (up to the saturation rate of the Gigabit Ethernet whith the UDP protocol with Jumbo Frame format)
    it takes care of APV25 setting (FE chips), data collection and visualization, including pedestal subtraction and zero suppression
    user friendly graphical interface
  Preliminary tests of the prototype (MICROMEGAS stable up to a gain of 20 k !)

## Slide 3: INFN activity – last 6 months
3 tasks on-going (cont.) :
test of novel materials for the THGEM PCB (for better performance, alternative to FR4):
  Reminder: previously, Permaglas established for high quality THGEMs
  Tested material: ARLON 25 FR (an epoxy laminate woven fiberglass reinforced, ceramic filled composites using a non-polar, low loss, thermoset resin), comparing with FR4
    Gain, resolution: ok
    Time evolution: very slow with ARLON
    material memory: reduced gain persistent for months after exposure to X-ray source!
    ARLON  NOT adequate for THGEMS
3. initial studies of the compatibility of an innovative photocathode based on NanoDiamond (ND) particles with the operation in MPGD-based photon detectors
  December 2017: meeting between the INFN Trieste and INFN Bari (the group who introduced the novel ND photocathodes)
    planning and methodology discussed in detail
    production of a few photocathode samples scheduled
energy res.
12.2 %
energy res.
11.9 %
Gain vs time
8 h
8 h

## Slide 4: INFN activity – future
Next future (2018):
  MICROMEGAS prototype with miniaturized pad-size
    Systematic laboratory (MICROMEGAS alone and coupled to 2 two THGEM layers)
    Preparation of the test beam studies (scheduiled for the end of 2018)
  Coupling of innovative photocathode based on NanoDiamond (ND) particles to MPGD photon detectors
    comparative measurements of QE in vacuum and in various gas atmospheres
    compatibility of ND photocathodes with operation in gases (dust release, if any)
    preliminary characterization of a MPGD equipped with the ND photocathode
  Corresponding MILESTONES:
    September 2018: The completion of the laboratory characterization of the photon detector with miniaturized pad-size.
    September 2018: The completion of the tests to establish the compatibility of the ND photocathodes with the operation of MPGD-based photon detectors.
Further future (> 2018):
  comparison of THGEM vs GEM photocathodes in order to select the best architecture for the photon detectors of the EIC RICH;
  further studies in order to enhance the IFB suppression in hybrid MPGDs;
  operation of hybrid MPGDs in fluorocarbon-rich gas mixtures;
  if the compatibility of ND photocathode and MPGD is established, further studies of MPGD-based photon detectors with ND photocathodes.

## Slide 5: INFN activity – complementary information
Personnel (globally equivalent to 3 FTE):
  From INFN Trieste:
    M. Baruzzo (Trieste University and INFN, master student)
    C. Chatterjee (Trieste University and INFN, PhD student)
    S. Dalla Torre (INFN, Staff)
    S. Dasgupta (INFN, postdoc)
    S. Levorato (INFN, Staff)
    F. Tessarotto (INFN, Staff)
    Y. Zhao (INFN, postdoc)
    technical personnel from INFN-Trieste foreseen according to needs
  From INFN BARI:
    Grazia Cicala (Bari University staff and INFN)
    Antonio Valentini (Bari University and INFN, professor)
External Funding
  2018 INFN support for this activity: 12 k €
    Reminder - 2017 INFN support : 13 k €